## Slide 1
Cellular planning and capacity
Notes: 1

## Slide 2: Cellular planning and capacity
To ensure complete area coverage with no dead spots, a series of regular polygons are assumed.
Based on simple geometry, the centre to centre distance between adjacent hexagons, x, is given by where R is the centre to vertex distance.
r= cos30*R
x=2*r =

## Slide 3: Cellular planning and capacity
An operator is allocated a certain bandwidth allocation, based on the type of radio system being used
This radio bandwidth is sub-divided into a number of frequency groups.
The number of frequency groups is defined by the cluster size
Here N=4 and each frequency group has 3.75 MHZ bandwidth

## Slide 4: Cellular planning and capacity
We can see network examples based on a cluster size N of 3, 4 and 7.
The figure shows how the cochannel reuse distance varies with cluster size.
As the cluster group gets larger, so does the distance between adjacent cochannel cells.
Clearly, the more interference a system can tolerate, the lower the required ratio and the smaller the resulting cluster size N.

## Slide 5: Hexagonal Axes and Co-ordinate System
The most convenient co-ordinate system for a hexagonal cell structure is using axes inclined at 60 degrees.
Assuming the origin to be at (0,0) and restricting u and v to integer values (u=i, v=j), the normalised distance to the cell centre is given by
Normalised so x= =1

## Slide 6: Hexagonal Axes and Co-ordinate System
To compute the number of cells per cluster, an arrangement of the form shown here is used.
The cells designated by the letter A are the six nearest cochannel cells (i.e. the first-tier) to the centre cell .
It can be seen that these cells are located at the vertices of the larger hexagonal cell of radius D. The radius of the larger cell D is given by

## Slide 7: Hexagonal Axes and Co-ordinate System

## Slide 8: Hexagonal Axes and Co-ordinate System

## Slide 9: Hexagonal Axes and Co-ordinate System
This equation is important since it relates the cell radius and the reuse distance to the cluster size.
The term D/R is referred to as the normalised cochannel reuse ratio. For example for a cluster size of 7, the ratio of D/R is 4.6

## Slide 10: Cluster size as a function of Cochannel Interference
The downlink of a cellular system can be modelled based on the wanted signal and the interference from the six surrounding ‘first-tier’ cochannel cells.
For a worst case scenario, the user is assumed to lie at the cell boundary (a distance R from the centre basestation) and the six first-tier interfering cells are all assumed to lie at a distance of D-R.
The signal power from the centre basestation is inversely proportional to the n-th power of the distance, where n represents the propagation path loss index

## Slide 11: Cluster size

## Slide 12: Capacity evaluation
The capacity of a cellular system is a function of the total bandwidth, the channel bandwidth, the cluster size and the cell area.
The total bandwidth for a cellular system is normally allocated by a regulatory body (such as Ofcom in the UK). Typically, this allocation is around 5-15 MHz per operator per network.
The channel bandwidth is defined as the average bandwidth required to support a single communications channel. For TDMA systems this value can be obtained by dividing the carrier bandwidth by the number of user slots.
The cluster size is a function of the system’s C/I tolerance and the cell sectorisation strategy.
Finally, since capacity is often quoted ‘per kilometre squared’, the average cell radius is also used in the formulation.

## Slide 13: Capacity evaluation
The general equation for capacity is therefore given by
The channel bandwidth can vary significantly depending on technology. Usually 25kHz per voice channel is assumed.
Capacity is also a function of the cell area, not surprisingly higher capacity can be obtained if smaller cell sizes are used.
To determine the number of subscribers that can be supported, the previous capacity equation can be used in conjunction with the average traffic density per user. As mentioned previously, the average subscriber creates approximately 0.02 Erlangs of traffic. Hence, capacity can be estimated with the following expression

## Slide 14: Microcellular systems
The concept of a microcell has been introduced into cellular networks to provide increased capacity within a limited radio spectrum allocation.
They refer to small cells (<1 km) in an urban area where the base station antennas are significantly lower than the surrounding roof tops.
Unlike conventional large cell scenarios, where base station antennas are placed on the tallest buildings, a microcell’s coverage area is largely governed by the effects of the surrounding buildings (i.e. by urban shielding).
Microcells often operate with lower transmit powers at the base station, and this further reduces the coverage area.
The lower transmit power, combined with the effects of urban shielding, results in a shorter co-channel reuse distance, hence cell frequencies can be reused more often in a given area. A high density of reuse cells will naturally increase system capacity.