## Slide 1: Delay (Many flavours, like milkshake) & The Bandwidth-Delay Product

## Slide 2: Total Delay
Q: How long does it take for a single bit to go from here to Australia?
A: It is the sum of multiple delay-causing factors
It takes some time to put a single bit on a link (Transmission Delay)
It takes some time for the bit to traverse the link (Propagation Delay)
In a path with many hops, the bit may have to wait at intermediate devices (Queuing Delay – Irrelevant at the Link Layer)

## Slide 3: Transmission Delay
If a link’s speed is 10Mbps then I can insert to the link 106 bits / sec
The time required to put N bits to the wire (or wireless medium)
Depends on:
  Number of bits
  The link’s capacity (in bps)

## Slide 4: Propagation Delay
How long does a single bit need
to cross to the other side?
Depends on physical distance and other physical characteristics of the medium (Physics!)
Link capacity (in bps) is irrelevant!

## Slide 5: Propagation Delay
Imagine a car driven down a motorway
There are no other cars
The motorway’s length is 70 miles
The motorway has a 70 miles/hour speed limit
A single car needs 1 hour to cross it
Double the number of lanes, the car still needs 1 hour to cross it
Double the length, the time to cross doubles.

## Slide 6: The Bandwidth Delay Product
Assume a link:
Capacity N bps
One-Way propagation delay of t sec.
The (one-way) BD product for this link will be N*t bits.
If a layer 2 protocol uses fixed-size frames, the BD product can be expressed as a number of frames.
The BD product expresses the maximum amount of data on the network circuit at any given time.

## Slide 7: BD Product
The BD product is an amount of data
It is NOT time
It is NOT speed
Possible exam question:
“Using a single sentence, describe what information we gain if we know the BD Product of a link.”
Your answer is automatically wrong if it starts with:
The time it takes…
The speed…