## Slide 1
Multipath propagation
Notes: 1

## Slide 2: Fast Fading
Amplitude and phase change significantly as user moves
  This can be attributed to the phasor addition of multipath signals
Notes: Frequency is rate of change of phase

## Slide 3: Arrival Phase of a ray (1)
We assume that a sinusoidal signal is received via 2 independent paths (rays)
  The arrival phase of each path will be different
The arrival phase of a ray is determined by:
  Electrical path length ()
  Carrier wavelength ()
Initial phase of ray
Path length
Carrier wavelength
Notes: Frequency is rate of change of phase

## Slide 4: Arrival Phase of a ray (2)
Equation for a given path:
Amplitude (distance dependent)
Angular frequency ()
As user moves, the path length varies, the phase of ray changes as well
If 2 rays arrive in phase --- constructive interference (PEAK)
If 2 rays arrive in anti-phase (180 degrees apart) --- destructive interference (FADE or CANCEL)
  Since many rays arrive at the receiver, usually the probability of cancellation is really small
Notes: Frequency is rate of change of phase

## Slide 5: Multipath Propagation
Various diffracted and reflected multipaths linking Rx-Tx
Urban multipaths from a Tx (Wills Building) to a mobile at the bottom of Park Street

## Slide 7: Multipath scenarios
Simplest path scenario
  Based on 2 arriving rays (paths)
Two paths have similar amplitude: Rayleigh scenario
  Usually we assume at least 8 multipaths
In many mobile scenarios, one multipath arrives at Rx with far more power than the rest (dominant path) – usually LoS case
  Also Non-LoS when we have a strong reflector
One path arrives with more power: Rician scenario
  Vector summation is more deterministic (less variations)

## Slide 8: Rayleigh Distribution
In-phase:
Anti-phase:

## Slide 9: Rician Distribution
One path arrives with more power --- dominant path
Amplitude and phase transients less severe
As amplitude ratio between rays increases, signal becomes more deterministic
The degree of variation is characterised by the K-factor

## Slide 10: K-factor
K-factor defines degree of variation
envelope power of dominant components
envelope power of random components
No dominant component (Rayleigh), then K-factor small/negative (dB)
A strong dominant path (Rician), then 5dB < K-factor < 10dB
Notes: All equations good for systems with dominant strong Line of Sight (satellite and microwave p2p comms…where multipaths with mobile radio apps not that good

## Slide 11: Envelope and Phase Variations (Rayleigh)
Assuming 8-ray scenario:
Deep envelope fades, are seen

## Slide 12: Envelope and Phase Variations (Rician)
Assuming 8-ray scenario:
Less severity in fading compared to Rayleigh
less severe fading compared to

## Slide 13: Rayleigh fading over rectangular area
Fading over a rectangular area (i.e. room)
Small movements in space result in changes in the envelope (amplitude)
Deep fades can be 40dB below the signal peaks

## Slide 14: Delay Dispersion (1)
Multipath signals arriving at the receiver, take unique paths
  Experience a different time of flight
The difference in the time of flight, results in time dispersion between the multipaths at the receiver

## Slide 15: Delay Dispersion (2)
Signal bounces off nearby buildings, resulting in 4 multipaths
  Multipath 1 is the shortest, has the shortest time of flight
  Multipath 4 is the longest with the longest time of flight
Four distinct pulses at Rx, resulting in time spread of
If time spread large compared to digital bit period: problems at Rx
As tx rate increases  bit period decreases  time dispersion becomes a limiting factor

## Slide 16: Power Delay Profile (1)
The time dispersive nature of the channel is characterised by the Power Delay Profile (PDP)
Obtained by plotting the power of each multipath against its time of flight
Sometimes, time of flight is normalised relative to the time of the first arriving ray
  time axis represents relative delay

## Slide 17: Power Delay Profile (2)
Theoretic indoor PDP shown
Usually, the first rays to arrive, have the largest amplitude (shortest distance)
  magnitude tends to fall away as the time delay increases (due to path loss, reflection/diffraction loss)
We quantify the degree of dispersion in
a channel by using its
Root Mean Square (RMS) delay spread

## Slide 18: RMS delay spread
rx’d amplitude of k-th ray after time delay seconds
time for half the power to arrive
(mean delay)
incorporates all information about the PDP, expressing it as single value
  Its magnitude allows comparison between differing channels & environments
Weak paths (with long delays) result in large rms delay spread
  usually discarded (below a power threshold relative to the strongest path – 20dB)

## Slide 19: Normalised RMS delay spread
Digital Transmissions: the value is normalised to the transmission bit rate or bit period
An unequalised digital system generates a BER of 1 in 1000 for a normalised rms delay spread of 0.1.
Equalisation: DSP performed to correct for time delay spread (or frequency selective fading)
Digital Modems, supporting high data rates, include some form of equalisation to account for the effects of delay spread

## Slide 20: Time dispersive/Frequency selective (1)
Maximum bandwidth supported without need of equalisation in time dispersive, or frequency selective channel, is known as Coherence Bandwidth
  The bandwidth over which the frequency response of the channel is flat
  The frequency separation required between two tones for the envelope fading correlation to fall to 0.5
Time dispersive/Frequency selective fading
  Bandwidth is large --- WIDEBAND channel
  Bandwidth of the channel > Coherence Bandwidth
  Short symbol period that allows all multipaths to get analysed (we get the symbol at every multipath at the Rx --- many copies of the signal)
Notes: Frequency is rate of change of phase

## Slide 21: Time dispersive/Frequency selective (2)
Flat fading
  Narrow bandwidth --- NARROWBAND channel
  Bandwidth of the channel < Coherence Bandwidth
  Symbol period is large relative to how long it takes the multipaths to arrive
    For example 5 sec for all multipaths to arrive, whereas the symbol time is 100sec
Power Delay Profile before
Now we look at the frequency domain channel response
Notes: Frequency is rate of change of phase

## Slide 22: Frequency Selective Channel
Deep notches with 5-7MHz width
Notch width inversely proportional to rms delay spread
In frequency domain: the time delay spread creates deep frequency notches
In time domain: the time delay spread produces Inter Symbol Interference (ISI)
ISI: signal is distorted due to one symbol interferes with subsequent symbols. Results in errors in decision device at Rx.
Notes: Frequency is rate of change of phase

## Slide 23: Exponential model
PDP assumed to follow an exponential profile  Approximated coherence bandwidth:
Notes: All equations good for systems with dominant strong Line of Sight (satellite and microwave p2p comms…where multipaths with mobile radio apps not that good

## Slide 24: Wideband System
Channel bandwidth is far in excess of the channel’s coherence bandwidth. Allows higher bandwidth and faster communication.
Narrowband System
Channel bandwidth is less than the channel’s coherence bandwidth.